## Slide 1: Midterm –mobot navigation
Team Delta : Saandeep Sreerambatla, Ahmed Bugra Aydin, Yuqi Hu

## Slide 2: Problem statement
We have a known position of the robot, we have to move to dock station1, then back to the initial position, then docking station 2, and come back to home pose.
Environment used :ROS, and Jinx robot in the lab for actual robot movement, and gazebo for simulation
Languages used: C++, Cmake.

## Slide 3: implementation
The entire navigation is performed using multiple nodes which will be explained below, for all the nodes starter code is provided, the references would be provided at the end of the presentation.
Node: Current State Publisher
This node is a used for previous assignment, this does publish the current state of the mobot , along with this also subscribes to odom and continuously publish the current state . This is very useful for validating the position of the robot, that is home pose should be 0, 0, 0

## Slide 4: Nodes Contd..
Lidar_alarm : The functionality of lidar_alarm is used from multiple assignments that it checks the entire environment using lidar_pings, and gives a alarm or warning where there is an obstacle in the vicinity.
Modal_trajectory_controller : This controller is closed loop controller , which controls the location of the robot by taking the help from amcl.
Des_state_publisher : This node publishes the desired x, desired y, desired heading and also the desired mode on where the robot is headed.

## Slide 5: Nodes contd..
Navigation_coordinator : This node is responsible for the actual movement of the robot. This used the trajectory builder node, (from the reference) for movement of the robot.
Traj Builder : This is an existing node, which computes the vector of states for the robot to travel.

## Slide 6: Observations
It is observed that the simulation environment is very useful for experimenting with the code.
It’s also quite well connected that, the code that runs on the simulator can easily be moved to Jinx without any modifications.
We faced few issues with AMCL , where the robot was behaving exactly opposite of what we instructed it to do.

## Slide 7
Not always, the home pose is 0, 0, 0 when the robot is moved back manually after e-stop
Faced issues with catkin_make on delta machines which Dr. Lee has fixed
Hardware issues such as issues with the battery, inverter, etc., were learnings for the entire team on different parts of the robot.
Could clearly understand the difference between writing code and seeing it working on a real physical machine

## Slide 8: References
Dr.Newman's Repo
https://github.com/wsnewman/learning_ros_noetic.git
https://github.com/wsnewman/learning_ros.git
https://drive.google.com/file/d/1Pd4r6FjKtktNDxQsUK1rWak3BtJsIeSH/view?usp=sharing